## Slide 1: Weather Radar ATMS 370

## Slide 2: Weather Radar
Weather radars can determine where precipitation is falling
Can also tell the intensity of the precipitation
Doppler radars can also determine the speed/velocity of precipitation toward or away from the radar.
Dual-polarization radars can determine precipitation characteristics.
Radars can track storms, fronts, and other major features

## Slide 3
RAdio Detection And Ranging
Weather radars emit pulses of electromagnetic radiation in the microwave part of the electromagnetic spectrum
Radar wave pulses hit and are reflected/scattered back from targets (often precipitation)
The time it takes to return tells the distance
The amount of return tells us about precipitation intensity and type

## Slide 4: Weather Radar History

## Slide 5: Radar Was An Important Tool in WWII for tracking aircraft. Serious Problem—Precipitation!

## Slide 6: WWII Radars

## Slide 7: After WWII, Meteorologists Experimented with Military Radars: Thunderstorms and Convection Clearly Seen

## Slide 8: Hurricanes Also Apparent, Including Eye Walls, Rainbands

## Slide 9: In the late 1950’s a national meteorological radar network was established (WSR-57).

## Slide 10: WSR-57 (no Doppler capability)

## Slide 11: During the 1970s and early 80s a lot of experimentation with Doppler Weather Radars
Can show wind shifts and circulations
Diagnose how wind changes with height
Particularly useful for showing the rotation in severe convection—the mesocyclone

## Slide 13
In the late 1980s,
the NWS put in a network of Doppler Weather
Radars:
NEXRAD
WSR88D
(Weather Surveillance Radar 88 Doppler)

## Slide 15
The National Weather Service has Installed Doppler Weather
Radars Across the Country
Available every 5-6 minutes

## Slide 16: Big Radar Advance in 2011: Dual-Polarization

## Slide 17: Can determine precipitation type and more

## Slide 18: Basics of Weather Radar

## Slide 19: Radar waves move at the speed of light (186,000 miles per second in a vacuum). Thus, the time from emission to return tells how far the object is away.

## Slide 20: The amount of radar signal returned tells one about the nature of the object: type and intensity of precipitation
Amount scattered back ~ D6 where D is the diameter of the target
Big objects (e.g., large rain drops associated with heavy rain)---big radar return
Small objects (small droplets)—lesser return
More objects—more return

## Slide 21: Thus, heavy rain with lots of big droplets give a big radar return!

## Slide 22
Pr = C |k2| Z
r2
Pr is the received power
R is the distance to a target
|k2] depends on the refractive and absorptive properties of particles
Liquid H20 ~.93, ice ~.21. Liquid water is seen better than ice!
C depends on the characteristics of the radar (e.g., emitted power, antenna type, emission power
Z is the radar reflectivity factor

## Slide 23: Z : Radar Reflectivity Factor
Summed over some volume
Only valid for targets small compared to the wavelength (l) of the emitted radiation
l radar ~1-20 cm (microwave)
raindrops: .5 to 2 mm, cloud droplets ~ .02 mm

## Slide 24: Z : Radar Reflectivity Factor
Conclusions:
Big precipitation drops are seen better than small droplets
Cloud droplets not seen well
Big fat birds are seen well

## Slide 25: Need a logarithmic scale
Since Z and Pr can vary by ORDERS OF MAGNITUDE, convenient to express using a logarithmic scale

## Slide 26: Reflectivity
A fancy name for the amount of radar signal that is returned by an object: reflectivity (Z) is given in units of dbZ
db or decibels-unit of power on a logarithmic scale
Precipitation intensity is proportional to Z (or dbZ)

## Slide 27: Example
Intensity of precipitation is color coded (units—dbZ)

## Slide 28: Reading a Radar Image (color scales can vary)
Black (white in some)-no precip
Grey and pink (5-20 dbZ)…light rain…not too bad.
Dark pink to green-moderate rain (20-35)
Yellows are heavy rain 40-50 (forget it)
Reds and higher (very heavy rain or hail)

## Slide 29: Radar Imagery is not observed or displayed for a level surface
Radars scan in azimuth ( 0 to 360 degrees) at a series of increasing scan angles from the horizontal.

## Slide 31: So radar image does not show a single level, but a sloping cut through the atmosphere
Thus, it is showing precipitation higher and higher up in the atmosphere as you move away from the center of the radar image.
https://www.youtube.com/watch?v=Yrq2TVdM8HI

## Slide 32: Radar imagery is generally shown on a polar-type chart with range circles at increasing distance
Higher
Lower
Radar
location

## Slide 33
Range circle every 100 km (60 miles)

## Slide 34: Radar Energy is Sent Out in Pulses
Pulse Repetition Frequency (PRF) of the radar system is the number of pulses that are transmitted per second.

## Slide 35: National Weather Service Scan Strategies (also called Volume Coverage Patterns, VCP). Takes 4-6 minutes for each VCP

## Slide 36: Also a clear air mode (VCP)
In clear air mode, the pulses are longer, resulting in more radar sensitivity
Scans take longer (about 10 minutes)
More coverage at lower elevation angles.

## Slide 37: In Clear Air Mode Can See Bird, Insects, and More

## Slide 42: Ornithologists Love Weather Radar

## Slide 43: Radar Beam Width
Radar beams are cone shaped and get wider with distance

## Slide 44: Vertical (and horizontal) resolution degrades rapidly with distance

## Slide 45: Important points
Shallow drizzle often does not appear on radar imagery, particularly when a distance away.
Can only see deep and high-level precipitation at a distance.
Radar beam can be blocked by local terrain.

## Slide 46: Beam Blockage

## Slide 47: Beam Blockage Obvious in the West

## Slide 48: Why You Generally Can’t See Drizzle: Beam Usually Too High

## Slide 49: The Radar Beam Position is NOT Always the Same: Depends the Density Structure with Height

## Slide 50
Less dense air
More dense air
Up

## Slide 51: Why does radar beam swing down?
Less dense air
More dense air
Up

## Slide 52: Radar beam moves faster in less dense air!
Less dense air
More dense air
Up
Moves faster
Moves slower

## Slide 53
faster
slower

## Slide 54: If air is warmer than normal (and less dense) near the surface, get subrefraction

## Slide 55: If cold air near the surface and warm air aloft (e.g., inversion) can get superrefraction

## Slide 56: Superrefraction can cause the radar beam to hit the surface very quickly for the lower scan angles

## Slide 60: Even under normal conditions, the lower beam can hit the surface!

## Slide 61: Composite Reflectivity: The Highest Reflectivity Above Each Point Using All Scan Angles

## Slide 63: Radar-based Echo Tops
Useful for finding the strongest convection

## Slide 64: Unambiguous Range (Ru)
Distance the radar pulse can travel roundtrip between pulses
Clearly related to the pulse repetition frequency (PRF) we already talked about.
The lower the PRF, the farther the radar pulse can move until the next pulse
/2PRF where C is the speed of light

## Slide 65: Unambiguous Range (Ru)
/2PRF where C is the speed of light
As PRF increases, the unambiguous range goes down.
Makes sense: if there a less time between pulses, the pulse can’t go as far (and back) before the next pulse is sent out.
When a pulse is received at the radar, is it a return from the last pulse or from one before?

## Slide 66: Modern Radars are Doppler Radars
Doppler radars can tell the speed of the target towards or away from the radar.
The wavelength/phase of the radar signal changes, depending the speed of the target towards or away from the radar.

## Slide 67: Same principle used in police radar guns

## Slide 68: Based on Doppler Effect: evident when a train or car passes. Frequency of sound changes.
https://www.youtube.com/watch?v=a3RfULw7aAY

## Slide 69: The Doppler effect (also Doppler shift) is the change in the frequency of a wave in relation to an observer who is moving relative to the source of the wave

## Slide 70: Doppler Effect for Weather Radars
The ”targets” are generally precipitation particles (rain drops, snow flakes)…but can include birds, bugs, and even tornado debris.
Meteorological targets generally move with the wind…so we get wind information from Doppler
radar.

## Slide 71: Radar Doppler Velocities Give Radial Wind Component toward or away from radar
NOT the total velocity vector

## Slide 72: Doppler Radar Imagery

## Slide 73: Similar polar plot as reflectivity Colors are wind speed towards or away from the radar

## Slide 74: Standard: Cold colors (blue/green) approaching, warm colors (yellow/red) leaving

## Slide 76: Which way are birds flying? Langley Hill Radar

## Slide 77: Which way are birds flying?

## Slide 78: No turning with height, no advection

## Slide 79: “ S “ shape: veering, clockwise rotation with height, warm advection

## Slide 83: Backing: Backwards S, cold advection
Cold Advection

## Slide 84: Dopper radar can identify rotation associated with tornadic thunderstorms: mesocyclones

## Slide 85: Rotation Seen on Doppler Radar

## Slide 86: One can figure out the TOTAL wind vector above each radar! How?

## Slide 87: Velocity Azimuth Display: VAD Wind Profiles

## Slide 89: VAD

## Slide 90: Dual Polarization Radar

## Slide 92: In addition to Reflectivity (Z), there are dual-polarization products such as ZDR, KDP, and CC

## Slide 93: ZDR

## Slide 94
Information about the shape and size of raindrops

## Slide 95: Good for finding hail shafts (ZDR~ 0)

## Slide 96: Correlation Coefficient (CC)
Measures the correlation between the horizontal and vertical back-scattered pulses from the scatterers within a sample volume scan of the radar

## Slide 98: KDP
The difference in phase shift between horizontal and vertical polarized returned energy.

## Slide 99: Dual-polarization information allows the determination of precipitation type and other characteristics

## Slide 100: Radars as Rain Gauges
It is possible to estimate precipitation intensity and precipitation accumulation from radar data.
This relationship has been studied extensively in many regions, seasons, and precipitation regimes.

## Slide 101: Z-R relationship (reflectivity-rainfall rate)
Different values can be used at various sites
Can calibrate using radar and rain gauge data

## Slide 102: Also a dual-polarization algorithm for rain rate estimation
Rainfall retrievals using combinations of reflectivity (Zh), differential reflectivity (Zdr), and specific differential phase (Kdp) are made.
Have advantages over traditional Z–R methods because more information about the drop size distribution (DSD) and hydrometeor type are available.
Generally better accuracy

## Slide 103
Dual Pol
Traditional Z-R

## Slide 105: My Favorite Radar App: Radarscope