## Slide 1: Weather Radar ATMS 370 2026

## Slide 2: Weather Radar
Can determine where precipitation is falling
Can also tell the intensity of the precipitation
Doppler radars provide the speed/velocity of precipitation toward or away from a radar.
Dual-polarization radars can determine precipitation characteristics.
Radars can track storms, fronts, and other major features

## Slide 3
RAdio Detection And Ranging
Weather radars emit pulses of electromagnetic radiation in the microwave part of the electromagnetic spectrum
Radar wave pulses hit and are reflected/scattered back from targets (often precipitation)

## Slide 4
Radar waves move at the speed of light (186,000 miles per second in a vacuum
Thus, the time from emission to return tells how far the object is away.
The amount of return tells us about precipitation intensity and type

## Slide 5: Weather Radar History

## Slide 6: Radar Was An Important Tool in WWII for tracking aircraft. Serious Problem—Precipitation!

## Slide 7: WWII Radars

## Slide 8: After WWII, Meteorologists Experimented with Military Radars: Thunderstorms and Convection Clearly Seen

## Slide 9: Hurricanes Also Apparent, Including Eye Walls, Rainbands

## Slide 10: In the late 1950’s a national meteorological radar network was established (WSR-57).

## Slide 11: WSR-57 (no Doppler capability)

## Slide 12: During the 1970s and early 80s a lot of experimentation with Doppler Weather Radars
Can show wind shifts and circulations
Diagnose how wind changes with height
Particularly useful for showing the rotation in severe convection—the mesocyclone

## Slide 14
In the late 1980s,
the NWS put in a network of Doppler Weather
Radars:
NEXRAD
WSR88D
(Weather Surveillance Radar 88 Doppler)

## Slide 16
The National Weather Service has Installed Doppler Weather
Radars Across the Country
Available every 5-6 minutes

## Slide 17: Big Radar Advance in 2011: Dual-Polarization Sent out microwave beams with two orientations

## Slide 18: Can determine precipitation type and more

## Slide 19: Basics of Weather Radar

## Slide 20: The amount of radar signal returned tells one about the nature of the object: type and intensity of precipitation
Amount scattered ~ D6 where D is the diameter of the target
Big objects (e.g., large rain drops associated with heavy rain)---big radar return
Small objects (small droplets)—lesser return
More objects—more return

## Slide 21: Thus, heavy rain with lots of big droplets give a big radar return!

## Slide 22
Pr = C |k2| Z
r2
Pr is the received power
R is the distance to a target
|k2] depends on the refractive and absorptive properties of particles
Liquid H20 ~.93, ice ~.21. Liquid water is seen better than ice!
C depends on the characteristics of the radar (e.g., emitted power, antenna type, emission power
Z is the radar reflectivity factor (how well a target scatters radar)
The Radar Equation

## Slide 23: Z : Radar Reflectivity Factor
Summed over volume
Only valid for targets that are small compared to the wavelength (l) of the emitted radar radiation
radar ~1-20 cm (microwave)
raindrops: .5 to 2 mm, cloud droplets ~ .02 mm

## Slide 24: Z : Radar Reflectivity Factor
Conclusions:
Big precipitation drops are MUCH seen better than small droplets
Cloud droplets not seen well
Big fat birds are seen well

## Slide 25: Big Radar Return

## Slide 27: Need a logarithmic scale
Since Z and Pr can vary over ORDERS OF MAGNITUDE, convenient to express using a logarithmic scale
Units of dBZ

## Slide 28: Reflectivity
A fancy name for the amount of radar signal that is returned by an object: reflectivity (Z) is given in units of dbZ
db or decibels-unit of power on a logarithmic scale
Precipitation intensity is proportional to Z (or dbZ)

## Slide 29: Example
Intensity of precipitation is color coded (units—dbZ)

## Slide 30: Reading a Radar Image (color scales can vary)
Black (white in some)-no precip
Grey and pink (5-20 dbZ)…light rain
Dark pink to green-moderate rain (20-35)
Yellows are heavy rain 40-50 Reds and higher (very heavy rain or hail)

## Slide 31: Radar imagery is generally shown on a polar-type chart with range circles at increasing distance
Higher
Lower
Radar
location

## Slide 32
Range circle every 100 km (60 miles)

## Slide 33: Radar Imagery is not observed or displayed for a level surface
Radars scan in azimuth ( 0 to 360 degrees) at a series of increasing scan angles from the horizontal.

## Slide 35: Radar images do not show a single level, but a sloping cut through the atmosphere
Thus, it is showing precipitation higher and higher up in the atmosphere as you move away from the center of the radar image.
https://www.youtube.com/watch?v=Yrq2TVdM8HI

## Slide 37: National Weather Service Scan Strategies (also called Volume Coverage Patterns, VCP). Takes 4-6 minutes for each VCP

## Slide 38: Also a clear air mode (VCP)
In clear air mode, the pulses are longer, resulting in more radar sensitivity
Scans take longer (about 10 minutes)
More coverage at lower elevation angles.

## Slide 39: In Clear Air Mode Can See Bird, Insects, and More

## Slide 40: Ornithologists Love Weather Radar (Particularly in Clear Air Mode)

## Slide 41: Clear Air Mode

## Slide 45: Radar Energy is Sent Out in Pulses
Pulse Repetition Frequency (PRF) of the radar system is the number of pulses that are transmitted per second.

## Slide 46: Radar Beam Width
Radar beams are cone shaped and get wider with distance

## Slide 47: Vertical and horizontal resolution degrade rapidly with distance

## Slide 48: Important points
Shallow drizzle often does not appear on radar imagery, particularly when a distance away.
Can only see deep and high-level precipitation at a distance.
Radar beam can be blocked by local terrain.

## Slide 49: Why You Generally Can’t See Drizzle: Beam Usually Too High

## Slide 50: Beam Blockage by Terrain

## Slide 51: Beam Blockage Obvious in the West

## Slide 52: The Radar Beam Position is NOT Always the Same: Depends on the Density Structure with Height (which changes!)

## Slide 53: Radar beams are refracted by density variations in the vertical
Less dense air
More dense air
Up

## Slide 54: Why does radar beam swing down?
Less dense air
More dense air
Up

## Slide 55: Radar beam moves faster in less dense air!
Less dense air
More dense air
Up
Moves faster
Moves slower

## Slide 56
faster
slower
LESS DENSE
Air
MORE DENSE
Air

## Slide 57: If air is warmer than normal (and less dense) near the surface, get subrefraction

## Slide 58: If cold air near the surface and warm air aloft (e.g., inversion) can get superrefraction

## Slide 59: Superrefraction can cause the radar beam to hit the surface very rapidly for the lower scan angles Provides false echoes near the radar

## Slide 61: Same time as previous radar echo.

## Slide 62: Model sounding at same time…..cold air near the surface

## Slide 63: Even under normal conditions, the bottom of the lower beam can hit the surface!

## Slide 64: Composite Reflectivity: The Highest Reflectivity Above Each Point for All Scan Angles

## Slide 66: Radar-based Echo Tops
Useful for finding the highest (and often strongest) convection

## Slide 67: Unambiguous Range (Ru)
Distance the radar pulse can travel roundtrip between pulses
Clearly related to the pulse repetition frequency (PRF) already talked about.
The lower the PRF, the farther the radar pulse can move until the next pulse
/2PRF where C is the speed of light

## Slide 68: Unambiguous Range (Ru)
/2PRF where C is the speed of light
As PRF increases, the unambiguous range goes down.
Makes sense: if there a less time between pulses, the pulse can’t go as far (and back) before the next pulse is sent out.
When a pulse is received at the radar, is it a return from the last pulse or from one before?

## Slide 69: Modern Radars are Doppler Radars
Doppler radars can tell the speed of the target towards or away from the radar.
The wavelength/phase of the radar signal changes, depending the speed of the target towards or away from the radar.

## Slide 70: Same principle used in police radar guns

## Slide 71: Based on Doppler Effect: evident when a train or car passes. Frequency of sound changes.
https://www.youtube.com/watch?v=a3RfULw7aAY

## Slide 73: The Doppler effect (also called the Doppler shift) is the change in the frequency of a wave in relation to an observer. The frequency change also produces a phase shift.

## Slide 74: Doppler Effect for Weather Radars
The ”targets” are generally precipitation particles (rain drops, snow flakes)…but can include birds, bugs, and even tornado debris.
Meteorological targets generally move with the wind…so we get wind information from Doppler
radar.

## Slide 75: Radar Doppler Velocities Give the Radial Wind Component toward or away from radar
NOT the total velocity vector

## Slide 76: Doppler Radar Imagery

## Slide 77: Similar polar plot as reflectivity Colors are wind speed towards or away from the radar

## Slide 78: Standard: Cold colors (blue/green) approaching air, warm colors (yellow/red) exiting air

## Slide 79: What is Wind Direction near the radar?

## Slide 80: Clear Air Return With Bird Echoes Which way are birds flying? Langley Hill Radar

## Slide 81: Which way are birds flying?

## Slide 82: Reminder about thermal wind and rotation of the geostrophic wind with height

## Slide 83: Temperature Advection and Wind Turning with Height
Backing (counterclockwise turning with height) of the the geostrophic wind: cold advection
Veering (clockwise turning with height) of the the geostrophic wind: warm advection
Thus, if the actual winds are ~geostrophic (not bad assumption above boundary layer) one can determine temperature advection from a single sounding—or Doppler Weather Radar

## Slide 84: Doppler Velocities No turning with height, no advection

## Slide 85: “ S “ shape: clockwise rotation with height, called veering, associated with warm advection

## Slide 86: “ S “ shape: veering

## Slide 90: Backing: Backwards S, cold advection
Cold Advection

## Slide 91: Doppler radar can identify rotation associated with tornadic thunderstorms: mesocyclones

## Slide 92: Rotation Seen on Doppler Radar
radar

## Slide 93: One can figure out the TOTAL wind vector above each radar! How?

## Slide 94: Measure the Doppler velocities around a radar by sweeping in azimuth

## Slide 95: Velocity Azimuth Display: VAD Wind Profiles

## Slide 96: VAD

## Slide 97: Dual Polarization Radars

## Slide 99: In addition to Reflectivity (Z), there are dual-polarization products such as ZDR, KDP, and CC

## Slide 100: ZDR

## Slide 101: Proves information on the shape of precipitation particles
Information about the shape and size of raindrops

## Slide 102: Good for finding hail shafts (ZDR~ 0)

## Slide 103: Correlation Coefficient (CC)
Measures the correlation between the horizontal and vertical back-scattered pulses from the scatterers within a sample volume scan of the radar

## Slide 105: KDP
The difference in phase shift between horizontal and vertical polarized returned energy.

## Slide 106: Dual-polarization information allows the determination of precipitation type and other characteristics

## Slide 107: Radars as Rain Gauges
It is possible to estimate precipitation intensity and precipitation accumulation from radar data.
This relationship has been studied extensively in many regions, seasons, and precipitation regimes.

## Slide 108: Z-R relationship (reflectivity-rainfall rate)
Can calibrate using radar and rain gauge data

## Slide 109: Also a dual-polarization algorithm for rain rate estimation
Rainfall retrievals using combinations of reflectivity (Zh), differential reflectivity (Zdr), and specific differential phase (Kdp) are made.
Have advantages over traditional Z–R methods because more information about the drop size distribution (DSD) and hydrometeor type are available.
Generally better accuracy

## Slide 110: Rainfall estimate from radar
Dual Pol
Traditional Z-R

## Slide 111: Dual Pol Better

## Slide 112: My Favorite Radar App: Radarscope